## Slide 1
1
Sources, origins and properties
Unit 6-1 Timbers

## Slide 2
Objectives
Explain the sources, origins and properties of a range of natural and manufactured timbers
Describe the advantages and disadvantages of manufactured boards and natural woods
Be aware of the social and ecological footprint of timbers

## Slide 3
Trees
Wood has been used as a building material and a fuel for thousands of years
Wood is a durable material, which should last a lifetime if well cared for
Our planet is home to over 23,000 different kinds of tree
  Explain the main difference between hardwood and softwood trees and the properties their timber may show

## Slide 4
Forests
Forests are vital to our ecosystem
Forests are described by their geographical location
  Alpine forests
  European Forests
  Amazonian Forests
  What type of trees would you find growing in each of these forests and why are they suited to that climate?

## Slide 5
What grows where?
Many species of tree can be bred to grow in areas other than their area of origin:
  Alpine forests are abundant with coniferous trees such as pine, cedar and larch which thrive in cooler climates
  European forests have a mix of soft and hardwoods where oak, beech, ash and birch flourish in a temperate climate
  Amazonian forests are home to many tropical hardwoods including mahogany, perhaps the most sought after timber due to its beautiful colour and grain structure

## Slide 6
Forestry management
If managed properly, forests are a sustainable source of timber
Well managed forests offer many benefits:
  Provide an environment for leisure activities
  Employment
  What other benefits do managed forests offer?

## Slide 7
Thinning forests
Managed forests contain trees of different ages
When trees are felled they are replaced with new seedlings
Young trees are thinned at around five years old
  Why is it common practice to 'thin' trees after five years?
  What do you think the thinnings might be used for?

## Slide 8
Felling
A tree is ‘felled’ when it is cut down
  Traditionally this was done using a hand axe or long saw
Modern felling uses a chainsaw or agricultural logging machinery that can fell a tree, de-branch it and cut it into equal length logs automatically
  What are the advantages and disadvantages of using mechanised felling methods over manual methods?

## Slide 9
Product mileage
How many miles might wood travel from tree to end user?
  What stages might there be on this journey?
  How might we ‘offset’ the carbon emissions generated at each stage?

## Slide 10
Timber conversion
Felled trees are cut into manageable lengths to be converted into timber planks and boards
  Timber is supplied in two main finishes: rough sawn or planed which will be covered in the next topic
  Traditionally the conversion process was very labour intensive but is now automated in many parts of the world

## Slide 11
Sustainability
Trees are one of our most valuable resources and yet we have not always treated them as such
  For a long time the rate of use has exceeded trees' rate of growth and this is still the case in some parts of the world
  Demand for more exotic timbers like teak and mahogany has given rise to a huge illegal logging industry

## Slide 12
Consequences of illegal logging
Illegal logging destroys vast areas of rainforest and causes desertification, deforestation and ultimately plays a role in global warming
  What might the be the possible consequences of desertification, deforestation and global warming?

## Slide 13
Timber provenance
Timber provenance is regulated by bodies such as:
  FSC® (Forest Stewardship Council®)
  PEFCTM (Programme for the Endorsement of Forest Certification)
In the UK, sustainably managed forests must be FSC or PEFC accredited
  How do you think the FSC and PEFC regulate the industry?

## Slide 14
Planning for the future
Designers and manufacturers have a responsibility to plan for a more sustainable future
Trend forecasting can help us identify what the future demands for timber might be
  How might ‘trends’ for different types of timber impact the industry?
  What trends affect timber supplies?

## Slide 15
Wastage
Much of the timber waste at saw mills can be used for the production of manufactured board
  Unusable parts such as bark and leaves can be composted or used as an agricultural mulch
  Economical use of timber is important in manufacture and offcuts can be used as packing pieces or for energy recovery
  Wood is recycled separately and is either reused, if high enough quality, or turned into fuel pellets for heating or for energy recovery through incineration

## Slide 16
Pollution
Trees are a non-polluting resource
While growing they absorb CO2 and release oxygen, giving forests the nickname ‘The lungs of the earth’
  When burned they release the trapped CO2 back into the atmosphere as smoke and soot
  ‘Slash and burn’ is a technique used to clear forests quickly for agricultural purposes – it destroys natural habitat and contributes to greenhouse gasses and global warming
  Discuss how other forms of pollution might occur when wood is transported, machined or finished or finished?

## Slide 17
Worksheet Task
Complete Task 1 or Worksheet 1

## Slide 18
Softwood
Softwood comes from coniferous trees like pine, cedar and larch
  These trees are faster growing than deciduous (hardwood) trees
  Softwoods are usually less dense than hardwoods and have a more open grain
  Softwood is used widely in the construction industry and for making furniture
  How might faster growth impact on the aesthetics and cost of softwood?

## Slide 19
Hardwood
Hardwood is sourced from deciduous trees like oak, birch, beech and ash
  Hardwood is slower growing and is therefore more expensive
  Sought after for its variety of colours and grain textures, it has desirable aesthetic and physical properties
  Most hardwoods are more dense and more hardwearing than softwoods
  Which hardwood is less dense than most softwoods and what is it used for?

## Slide 20
Working properties
In addition to hardness, toughness and durability, covered in Unit 4, you need to know the following:
  Elasticity - will it return to its original shape after being compressed or stretched?
  Tensile strength – the amount of load it can withstand when being pulled in opposite directions
  Compressive strength – the amount of load or ‘compression’ it can withstand when being pressed on two or more sides

## Slide 21
Physical characteristics
For each timber you need to know about:
  Knots
  Colour
  Density
  Grain structure
    Other than the specific species of tree, what factors may affect the physical characteristics listed?

## Slide 22
Timber in detail
Natural timbers vary dramatically
  Knots are the most common natural defect and can be a point of weakness or beauty depending on the viewpoint
  Softwoods, such as pine, larch and cedar, can seep resin at the knot which can stain and discolour
  Colour variations are an important feature - many woods are prized because of the natural tones in their grain
  Softwoods are usually whiter in colour and many yellow with age – hardwoods come in many tones from white through the browns and reds to a near black
  Which black wood, traditionally used for the black keys on a piano, is now on many endangered lists?

## Slide 23
Grain and density
Grain and density are linked but not the same
  Grain is the name given to the natural arrangement of wood fibres – it is the result of a number of factors including the type of tree, where it’s grown, how it’s sawn, how it’s finished, the age of the tree when felled and the time since being sawn
  Density is how close or open the grain structure is – this is determined by the type of tree and growing conditions
  Balsa is open grained hardwood and not dense whereas a redwood is a softwood and is very dense

## Slide 24
Timber grain structure
Hard and softwoods have a different grain structures
  Hardwoods are angiosperms and produce encased seeds such as fruits and nuts
  Hardwoods contain both fibres and pores but have very few tracheids, which are the cells that transport water and minerals
  Softwoods are gymnosperms - seeds are not enclosed but released from cones
  Softwoods don’t have pores, only tracheids make up the fibres of the wood
  How might the grain and density of hard and softwood be affected by annual growth rings?

## Slide 25
Specific properties in woods
First, let’s remember the woods covered in Unit 4
  Beech is tough and very durable with a fine finish
  Oak is tough, hard and durable with a variable grain
  Pine is lightweight and easy to work with
  Mahogany is durable and fairly hard with a distinctive grain
  Balsa is a soft and lightweight wood used for modelling
  Cedar contains natural oils which offer water resistance
Which are hardwoods and which are softwoods?

## Slide 26
Additional wood species
You also need to know about:
  Birch – A pale, fine, densely grained stable and durable hardwood used in furniture and to face plywood
  Ash – A very tough but flexible wood, which is shock resistant; useful for tool handles and in sports equipment
  Jelutong – A low-density wood that is used for pattern making and carving as it is easy to work
  Larch – Tough and hard, and with good resistant to rot, it’s a sought after wood for boat building and garden structures
Which one of these is a softwood?

## Slide 27
Manufactured boards
Manufactured boards come in large sheets, often made from waste or recycled wood with adhesives
  Manufactured boards are usually produced using lamination or compression techniques
  Manufactured boards are often covered with veneers of higher quality timber
  Why do you think manufactured boards can be classed as 'composite materials'?

## Slide 28
Laminated boards
Lamination is the technique of layering materials using heat, pressure and adhesives
  For plywood (covered in Unit 4) thin veneers are layered with the grain direction of each layer at 90° to each other
  Why are an odd number of layers used?
  How does lamination improve the material’s properties?
  Are there are any aesthetic advantages of laminated manufactured boards?

## Slide 29
Compression
Heat and pressure are used to bond adhesives to wood shreds, chips or pulp to produce large boards
  MDF (covered in Unit 4) uses fine dust and adhesive to give a smooth finish
  Chipboard used small chips of natural wood with adhesive to make a cost effective sheet material used in flooring and flatpack furniture
  Neither are good with moisture but can be covered with a melamine or Formica® laminate to improve aesthetics and physical properties
  Why are compressed boards weaker than laminated boards?

## Slide 30
Using manufactured board
Advantages | Disadvantages
Available in large sheets with few faults or defects | Adhesives used in manufacture can be hazardous when inhaled and damage the environment
Aesthetic flaws like knots can be eliminated, boards require very little finishing | Adhesives used in manufacture can blunt tools quickly
Made of wood that might otherwise go to landfill | Many traditional woodworking joints cannot be used and the edges are hard to finish well
Available in a vast range of surface finishes | Boards are prone to absorbing moisture which affects structural integrity

## Slide 31
Recycling and disposal
What happens to products made from wood and manufactured boards at the end of their useful life?
  Many adhesives, finishes and components used in wood products are not biodegradable
  Some wood products may be disassembled and parts recycled
  Products may also be ‘up-cycled’ and turned into something else
  How could designers help prevent wood products ending up in landfill?

## Slide 32
Kit house construction
Complete Task 2 on Worksheet 1

## Slide 33
Plenary
Forestry is the managed growing of trees for the timber industry
When trees reach maturity they are felled using a chainsaw or industrial cutting machines
  What happens next during the rest of the lifecycle of a tree used for timber?
  How do ecological and social factors play a part in timber selection?