## Slide 1
2
Selection and reinforcement of materials

## Slide 2
Objectives
Explain the different factors that influence the selection of materials including environmental, aesthetic, cost, social, cultural and ethical issues
Demonstrate an awareness of the influence of forces and stresses on natural and manufactured timbers

## Slide 3
Starter – Know your timber
Identify the types of timber by their aesthetic factors:
  Look at the grain colour and density and perceived texture – state which of the following is pine, oak, beech and mahogany

## Slide 4
Manufactured boards
Identify the types of manufactured board shown below and describe their aesthetic features
  What can be done to improve their aesthetic qualities?

## Slide 5
Timber selection
Timber is selected both for its aesthetic qualities and for its working properties
  Wide range of colours, grain types and textures
  Different timbers have different physical properties
  Available in a wide range of stock sizes and profiles
  Made well, wooden products have longevity
  Wood can be finished or treated to make it more durable
  Why might oak be chosen over pine for floor boards?

## Slide 6
Choice of material
A day in the life of a child’s toy is a tough one!
  They are thrown, dropped in water, left outside, stood on and chewed
  Justify a suitable type of wood to make a child’s toy

## Slide 7
Aesthetic factors in woods
Wood is a beautiful natural material and many varieties are highly sought after
  You need to know about a range of woods and be aware of their aesthetic characteristics:
  Form – the physical make up of a particular timber
  Colour – the tones in the grain and how they can be enhanced
  Texture – the density and the closed or openness of the grain

## Slide 8
Natural or manufactured
The type of material a product is made from will also influence the price of the end product
  Similar products may be made from different timbers to appeal to different markets
  Some timbers are traditionally used for certain products
  Which timber would you select to make a gate? Give two reasons why

## Slide 9
Engineered timber
Manufactured or engineered wood has many advantages over solid wood
  Mixed with adhesives giving greater strength and stability
  Ideal for use in construction, industrial and domestic use
  Efficient in its use of mixed materials and utilising waste wood
  It can be made in a large format sheets – not limited by the diameter of a tree trunk
  Name the disadvantages of using manufactured board

## Slide 10
Flat-pack furniture
Self-assembly products are well suited to manufactured boards
  They are generally less expensive than handmade items
  Arrives boxed, making it easier to store and transport
  Relatively straightforward to assemble with a basic tool kit
  What properties of manufactured board make it suitable for flat-pack products?
  Why do you think it may be less appealing in terms of aesthetics?

## Slide 11
As well as aesthetic factors, there are many other considerations when selecting wood
You need to know about:
  Environmental considerations
  Availability of supply
  Cost implications
  Social factors
  Cultural and ethical considerations

## Slide 12
Environmental factors
While a tree is growing and during its life as a product, timber affects the environment
  The long-term sustainability of timber is vital, buying from reputable, managed forests helps sustain our supply
  Avoid using woods on ‘endangered’ or ‘at risk’ lists
  Buy goods and materials that are manufactured locally if possible and look out for the ‘Grown in Britain’ and ‘Made in Britain’ logos or products
  How can expensive natural wood be made to go further?
  Name two organisations supporting sustainable forest management and timber production

## Slide 13
Genetic engineering
Manipulating a tree’s genetic structure can make it more economically viable
  Trees can be made to grow faster and straighter
  What other characteristics could be modified to enhance the properties of timber?
  How might trees be adapted to cope with the effects of global warming?
  Why do some people not agree with genetic engineering and modification?

## Slide 14
Seasoning
Seasoning timber reduces its moisture content
The two methods of seasoning are air or kiln drying
  What are the environmental advantages of air drying timber?
  Aside from being faster, are there any other advantages to kiln drying?

## Slide 15
Reuse through upcycling
Using products again is the best way to extend their life and ‘upcycling’ has become very fashionable
  Pallets and crates are a readily available source of good quality timber which can be used for many useful projects
  What did the table in this picture used to be?

## Slide 16
Sourcing materials
Designers and manufacturers need to ensure a constant and reliable supply of materials
  Where possible, they use stock materials, meaning that standard sizes and types will be readily available
  When using specialist materials they need to know the lead times as these may take longer to procure
  Disease can seriously affect trees, e.g. Dutch Elm disease is a fungus that almost wiped-out the UK’s elm trees
  Horse chestnuts are currently suffering from leaf-miner moth, bleeding canker and leaf blotch fungus – in just 15 years conkers may be history!

## Slide 17
Hurricanes & storms
What might be the impact of hurricanes and severe storms on timber supply?

## Slide 18
Which wood and why?
Complete Task 1 and 2 of Worksheet 2

## Slide 19
Cost factors
Many factors affect the cost of timber other than the available supply and the level of demand
  The quality of materials selected is a leading factor with many timbers being graded
  Wood flooring is graded by the number of knots or blemishes it contains; fewer knots means higher grade and price
  Construction timber is graded based on the load it can take
  For example, C16 grade timber is cheaper but weaker than C24 which has fewer defects, is stronger and can bear heavier loads

## Slide 20
Other cost implications
Manufacturing processes and treatments all affect cost
  How would the following factors affect the cost of building this tree house?
    Machine routed ‘tongue and groove’ panelling for the walls and floor
    Hand carved cedar roof tiles
    Fire retardant coating to all timber
    Tanalised timber to offer protection against rot and infestation from bugs
    Rust proof zinc coated screws and hinges

## Slide 21
Suitable design
Design conventions are not necessarily the same across all cultures
Different things appeal to different social groups
  Colours have different meanings
  Imagery can be interpreted very differently across the globe
  One product may not meet the same design needs in other countries
  How might objects and furniture in a British dining room differ from those in Japan?

## Slide 22
Trends in timber
Trends and fashions in timber products are influenced by several factors including:
    Aesthetics
    Economics
    Environmental issues
    Media coverage and fashion
  What timber-based materials would you describe as currently ‘on trend’?
  What could now be described as’ old-fashioned’ and why?
  What factors make a product popular?

## Slide 23
Cultural and ethical factors
Designers and manufacturers have responsibilities when designing and making products – they should:
  avoid causing offence
  make products suitable for the intended market
  consider the consumer society
  be aware of the effects of mass production
  be aware of built-in product obsolescence
  In what ways might this wooden roulette wheel be inappropriate for some international markets?

## Slide 24
Our consumer society
Mass production means that manufacturers can produce large numbers of products:
  quickly
  consistently
  accurately
  and at a much lower cost
This has created greater choice, but helped fuel a ‘consumer society’
  Discuss whether choice and availability are always good things

## Slide 25
Design
Designers must know their intended market when designing wooden products - this includes:
  users’ expectations, including the expected life of a product
  users’ needs
  the economic environment
Some products have ‘built in obsolescence’
  How long should this garden furniture last and why?
  How might obsolescence be built in and how products be made to last longer?

## Slide 26
Worksheet 2
Complete Task 3 of your Worksheet

## Slide 27
Timber processing
Timber is sawn and seasoned before use
As it dries, timber releases stresses and forces from the growing process, often causing faults
  Faults can weaken the wood making it unusable, resulting in wastage
  Wastage can be costly for the manufacturer and the environment
  How could wood wasted in the production of planks and boards be recycled?

## Slide 28
Faults
The faults that can occur as timber dries include:
  Bowing
  Splitting / cracking
  Springing
  Cupping
  Twisting

## Slide 29
Reducing faults
Faults can be minimised through careful storage and management
  Why is kiln dried timber less prone to faults than air dried?
  Why is the end grain of timber planks often covered with a special sealant?

## Slide 30
Forces and stresses
Both natural and manufactured timber products will experience forces and stresses in use
Which stresses does a wooden diving board experience in use?

## Slide 31
Defining forces
Work in pairs to define these five key forces:

## Slide 32
Stressed out
Some timber beams for construction come ‘pre-stressed’
  Lamination under pressure is used to created both straight and curved structures which can be made incredibly strong and stable
  As the timber beam is stressed during manufacture it is able to cope with the greater forces in use
What would be the advantage of using pre-stressed beams for a curved roof?

## Slide 33
Feel the force
Softwood is commonly used for frame structures
  Most wooden components can cope with both tension and compression as long as the structure is sound
  The roof truss pictured has to deal with compression & tension
  Braces and ties are used to add structural support
  What shapes are good for adding strength to structures?
  What is the difference between a brace and a tie?

## Slide 34
Brace and ties in action
Ties and braces are used to strengthen structures
  Ties are used in a structure to stop it moving outwards and are generally kept under tension
  Steel is often used for ties due to its high tensile strength
  Braces are used in a similar way but tend to be under compression
  Old buildings are sometimes seen braced with big timber structures to prevent collapse

## Slide 35
Shear agony
A shear force occurs when opposite forces act on an object in a direction perpendicular to its length
  Timber is generally very good at resisting a ‘shear’ force along the grain but not good across the grain
  Planks tend to snap when subject to shear force across the grain but flex and bend along the grain
  Occasionally, trees can be seen damaged by strong gusts of wind creating a shear force and snapping their trunks

## Slide 36
Give me strength
Timber and manufactured boards sometimes need reinforcement or strengthening to perform certain functions
This can be done in many ways including:
  lamination
  adding braces or tie bars
  embedding composite materials
  How could adding a GRP layer to these wooden skis improve performance?

## Slide 37
Plenary
As part of the ‘consumer society’ we are responsible for the buying decisions we make
You are in the market for a new study desk - discuss the pros and cons of buying:
  a cheap but ‘on trend’ flat packed desk from a leading furniture store
  or
  a second hand solid wood ‘retro’ desk from an online auction site