## Slide 1
3
Material stock forms and production

## Slide 2
Objectives
Be aware of commercial stock forms, types and sizes of timber-based materials and components
Understand specialist techniques, processes tools and equipment used for wasting, abrading, shaping, fabricating, constructing and assembling

## Slide 3
Working with timber
Timber and board materials are widely used in the school workshop
  They are readily available
  They can be cut and shaped using common tools and machines in the workshop
  They can be formed and bent using jigs and moulds
  They can be joined using a variety of joints and fixings
What other factors do you think make timber based materials a popular choice for the school workshop?

## Slide 4
PPE
What common personal protective equipment is required in the workshop when using different tools, machinery, materials and products?
  What additional precautions might be required?

## Slide 5
Timbers and components are commercially available in specific forms, types and sizes
  Planks, boards and standard mouldings
  Sold by length, width, thickness diameter and weight
  Standard components such as woodscrews, hinges and knock-down fittings
  What are the advantages of having regular stock forms, types and sizes of components?
Standard stock forms and sizes

## Slide 6
Standardisation
Timber comes in a range of standardised sizes
  Initially standardised sizes were imperial
  The UK now works in the nearest metric sizes (millimetres 'mm') to the old standard imperial sizes
  Lists of standard sizes are widely available as are conversion charts and apps
  Why is standardised sizing so important?

## Slide 7
Rough sawn timber
Planks and boards are stocked with different finishes
Rough sawn, planed all round (PAR) and planed square edge (PSE) are the most common
  Rough sawn is how the timber has all the marks from the circular saw or band saw used in the saw mill or timber yard
  It often has a rough finish and the saw marks are frequently visible
  Rough sawn is used for external use as it absorbs preservative well, also used in construction and areas where a smooth aesthetic is not required
  Sanded rough sawn ‘shabby chic’ furniture is very fashionable

## Slide 8
Rough sawn to PAR/PSE
Rough sawn planks are planed to achieve smooth flat and square forms
  Planed all round has a very slightly curved edge which reduces splinters and is easier to handle
  Planed square edge has a sharp edge where a tight fit is required
  PAR or PSE timber will be about 2-3mm smaller per face than the quoted nominal size
  Why is this – and approximately how big would a plank 150mm x 50mm actually end up?

## Slide 9
Timber sizes
Sawn timber comes in a variety of different sizes and sections
You need to know about:
  Planks
  Mouldings
  Dowels
  Sheets
  Which dimensions would you need to know to order dowels?

## Slide 10
Standard mouldings
Mouldings are decorative timber components with a shaped profile
  Where in a house are mouldings commonly used?
Mouldings can be made from natural timber or manufactured boards
  How are mouldings produced?
  How might they be pre-finished?

## Slide 11
Board and sheet sizes
Manufactured board comes in standard sizes most commonly:
  Full sheet - 2440mm x 1220mm (imperial 8 x 4 foot sheet)
  Half sheet - 1220mm x 610mm
Suppliers often offer to cut larger boards to size
  Why is it important to plan your requirements before cutting a board?

## Slide 12
Cross-sectional area
The chart shows some standard planed timber sizes
  Lengths tend to be in multiples of 300mm starting at 1.8m, however shorter lengths can be obtained, especially for dowel
  Actual sizes will vary between different timber suppliers

## Slide 13
Ironmongery
Ironmongers and DIY stores stock fittings and fixtures such as nails, screws and hinges
  These items also come in standard sizes
  Many hinge types are available for different jobs including:
    Butt hinge
    Flush hinge
    Butterfly hinge
    Concealed hinge
    Piano hinge

## Slide 14
Wood fixings and components
There are many ways to join timber together including:
  Screws and nails
  Dowel rods
  Hinges
  Adhesives
  What are the advantages of 'countersinking' a screw?
  If using nails to reinforce a timber joint, why might you angle them?

## Slide 15
Knock-down fittings
Knock down fittings (KDF) are often used for self-assembly furniture and kitchen carcasses
  Why do many people favour flat-pack furniture over pre-assembled pieces?
  What tools may be required to assemble flat-pack furniture?
Connecting or block fitting
Cross dowel fitting
Cam lock fitting

## Slide 16
Flat-pack furniture
Complete Task 1 of Worksheet 3

## Slide 17
Specialist tools and equipment
Specialist hand tools can be used to accurately remove or ‘waste’ and shape wood
  Name these tools used for wasting and shaping

## Slide 18
Wasting, shaping and abrading
Specialist hand tools include:
  Planes, chisels, saws, surforms and rasps
  Surforms and rasps remove material very quickly but leave a rough finish
  Abrasive paper and sanding tools are used to prepare a smooth surface for finishing
  If you had three grades of glass paper – 80 grit, 120 grit and 200 grit, which one would you use first, which one second and which one would you use last?
  Suggest the best sanding technique for getting a piece of wood ready for varnishing

## Slide 19
Cutting
Timber can be cut using a variety of tools and machines including:
  Hand saws
  Powered saws
  Machine saws
  Routers and multi tools
  The phrase 'measure twice, cut once’ is often used by crafts people – What do you think this means?
  Name the types of hand saws that you’ve used and describe the cutting techniques

## Slide 20
Drilling
Several different types of drill are commonplace in a workshop including:
  Hand drills
  Corded and cordless powered drills
  Pillar drills/drill presses
Cutting tools are called drill bits and include:
  Twist bits
  Augers
  Flat / spade bits
  Forstner bits and hole saws

## Slide 21
Mortising
Mortises can be cut by hand or by machine
  Like drilling, mechanical mortising works by plunging a spinning cutting tool vertically into the wood
  A drill bit rotates inside a hollow chisel is and is used to create a straight sided slot
  The work piece is moved horizontally and the plunging is repeated to create a slot
Mortising is used for:
  Creating ‘mortise and tenon’ joints
  Creating housings for mortise locks

## Slide 22
Routing
Routers are versatile power tools which can be used with a range of accessories
  Used to machine profiles and joints and cut slots and holes of various depths
  Handmade or bought-in jigs increase speed and accuracy
  CNC routers can be used to automate the routing process

## Slide 23
Planing and chiselling
Timber is wasted in order to produce accurate surfaces or rebates
This is done using planes:
  Jack planes
  Smoothing planes
  Block planes
And chisels:
  Mortice chisels
  Bevelled chisels
  Carving chisels

## Slide 24
Carving
A skilled craftsperson can develop the ability to carve wood with great accuracy and skill
  Using speciality tools such as chisels and knives, wood is shaped by hand into incredibly intricate shapes

## Slide 25
Wood turning
Lathes are used to 'turn' wood whilst it is shaped with a cutting tool
  Face plates and chucks are used for bowl shaped and larger pieces
  Turning between two centres (pictured) is used for spindles and long thin work
  The speed of the lathe is adjusted depending on the size of the piece
  Common cutting tools are scrapers, gouges, chisels and parting tools
  Why use a slower speed when turning a large bowl or dish?

## Slide 26
Chuck & faceplate turning
Turning with a chuck or faceplate holds larger work more securely
  With both of these methods the material is secured at one end only
  This gives flexibility in terms of the forms that can be created e.g. bowls, vases, domes
  The workpiece is either screwed to the faceplate or clamped in a chuck
  How would the shape of the product affect the turning method used?

## Slide 27
Material addition or forming
The opposite to wasting material is addition or forming
  This involved building up materials in specific ways to create the desired shape or form
  Usually, a combination of wasting and addition is used for most prototyping and product manufacture
You need to know about:
  a range of wood joints
  lamination and the use of a bag press
  adhesives
  adding veneers

## Slide 28
Wood joints
Wood joints are widely used where a strong or visually appealing joint is needed
  Adhesive and often other mechanical fixings such as pins, splines and biscuits are used to strengthen joints
  Which is the most commonly used adhesive for bonding wood joints and what are its benefits?
  How could you protect work from marking when using clamps?
Butt joint
Dowelled joint
Mitre joint

## Slide 29
More wood joints
Stronger wood joints have a greater surface area for adhesive and have a physical advantage
  Describe the physical advantage for each joint shown and name a potential use
Housing joint
Mortise and tenon joint
Dovetail joint
Lap joint

## Slide 30
Worksheet 3
Complete Task 2 of your Worksheet
  You should be familiar with common drilling, sanding, cutting and joining techniques and tools

## Slide 31
Lamination
Laminating involves layering and is often used to create curved components
  Strips of timber are glued and placed over a jig or former
  Either clamps or a vacuum press or bag are used to exert pressure on the laminate while the adhesive dries or cures
  Why is a laminated structure stronger than regular timber?

## Slide 32
Preparation the mould
The design, manufacture and preparation of a mould is crucial to a successful lamination
  Moulds are often covered in wax or parcel tape to prevent the laminate sticking to the mould
  The mould must allow for the thickness of the laminate
  Even coatings of glue give uniform strength to the laminate
Wax/parcel tape
Outer veneer
Inner veneers / flexiply
Former must allow space for veneers

## Slide 33
Using a vacuum bag
Lamination often calls for a two-part former but a vacuum press offers an alternative forming method
  Laminate is placed on a one-part mould and encapsulated in a heavy duty polythene bag
  A pump sucks the air from the sealed bag
  The resulting atmospheric pressure forces the laminate into position
    What are the pros and cons of using a vacuum bag?

## Slide 34
Rotational veneer production
Veneering is a form of lamination
Natural veneer can be made by rotating a tree trunk on a large industrial machine similar to a wood lathe
  This creates a long ribbon of veneer that can be cut to length
  Synthetic veneers are often made from melamine formaldehyde

## Slide 35
Veneering
Veneers are often added to manufactured boards to improve their aesthetic appearance
  Natural or synthetic veneers are glued to the main material under pressure using a veneers press or a vacuum bag
  Contact adhesive is commonly used for bonding veneers

## Slide 36
Worksheet 3
Complete Task 3 on your Worksheet

## Slide 37
Plenary
Why are materials available in stock forms, types and sizes?
For the chair pictured, discuss where different processes of wasting and addition would occur
  What tools, equipment and materials would be used to complete these processes?