## Slide 1
4
Material processing and finishing

## Slide 2
Objectives
Describe the different scales of production used to manufacture commercial products
Explain how materials are cut, shaped and formed to a tolerance and with minimum waste
Learn about the preparation for, and application of treatments and finishes to enhance functional and aesthetic properties

## Slide 3
Mechanisation and automation
Automated machinery has changed the way industry manufactures timber-based products
  Improvements in manufacturing methods have been embraced by designers
  Stringent quality control methods have increased consistency and accuracy
  Increased availability of manufactured boards means products can be batch, mass or continuously produced
  Discuss the differences between ‘mechanisation’ and ‘automation’

## Slide 4
Scales of production
Depending on the specific product, timber-based products are produced on different scales
  One-off or ‘bespoke’
  Batch production
  Mass production
  Continuous production
  Think of examples of products which would be suitable for each scale of production

## Slide 5
One off or bespoke
A cabinet maker may be commissioned to make a special piece of furniture for a client
  It will be predominantly handmade
  It will take time to make and the client is often involved in decisions
  High value materials may be used
  The design will not be repeated
  The end product will be more expensive but unique
Bespoke items are usually made by very small companies or a single craftsperson

## Slide 6
Batch
In batch production, runs of anything from more than one to thousands of identical products are produced
  Jigs, templates, fixtures, moulds, formers and patterns are used to speed up production
  Materials are purchased in bulk
  Skilled and semi-skilled labour used
  Limited runs with lower unit cost
  Simple production lines with some automation but still very flexible
  Seasonal goods tend to be batch produced – why is this?

## Slide 7
Jig, template, pattern, fixture
These are used to save time and increase accuracy - especially common in batch production
  Note: some terms are interchangeable and even have different meanings between material areas and industries
  Patterns – can be full size guides (or collection of) on paper, card or hardboard and include accurate information for drilling, cutting etc., but a pattern is also the term for a wooden shape used for casting
  Templates – can be more permanent than a pattern; this will often be a piece of board material cut from a pattern
  Jigs and fixtures – are used to hold materials to be cut, drilled or machined accurately and safely

## Slide 8
Mass and continuous production
Products made in very high numbers or produced continuously require:
  larger plants and use production or assembly lines
  shift work to facilitate 24/7 production
  a high level of automation including expensive tooling and machinery
  systems for quality control
  The downside is less flexibility for product diversity and slow to respond to change
  What timber-based products are likely to use these levels of production?

## Slide 9
Commercial manufacturing
Mass produced timber components are often made using CAM (computer aided manufacture)
  This enables large quantities of equal-sized parts or products to be produced
  CAD (computer aided design) files are saved and reused or adapted to save time

## Slide 10
Commercial routing
CNC machinery can cut, drill, shape, mill and profile manufactured or natural timbers very efficiently
  Screw holes, slots and patterns can all be cut in one process
  Machines can accommodate big sheets of material
  Machines work quickly and efficiently enabling a product to get to market swiftly
  What other advantages does CNC routing offer over hand cutting?

## Slide 11
Commercial turning
CNC wood lathes produce cylindrical components
  Once programmed, they are very effective at producing complex shapes and spirals
  Ideal for repeat production
  Lathes can accept large and long pieces of material
  What disadvantages would the introduction of CNC machinery present to a skilled workforce?

## Slide 12
Bought-in components
In all levels of production some fittings may be bought in from other manufacturers
They include:
  Hardware
  Electrical components
  Digital components
  Specialist parts
  In the production of hardwood kitchens, what parts do you think might be bought in?

## Slide 13
Sub assembly
Sometimes parts of a product are sub-assembled in separate ‘cells’ or offsite, prior to final assembly
  Allows manufactures to outsource parts
  Makes use of specialist skilled labour
  Increases efficiency and quality
  What parts of this chair could be sub-assembled?

## Slide 14
Worksheet 4
Complete Task 1 on your Worksheet

## Slide 15
Quality Control (QC)
The process where products are checked to ensure they meet the design specification
They should also:
  function correctly
  be free of defects
  be consistent and accurate
  meet set size tolerances
  In pairs, write a QC checklist for the child's shape sorter pictured

## Slide 16
Tolerance
Tolerance is the amount a specific dimension or property is permitted to vary
  This can apply to hole depth, length, angle, thickness, weight and elasticity
  Go-no gauges can be used to test components to see if sizes fall within tolerance
  If parts are not within the specified tolerances they are corrected, discarded or recycled
  Why is it important for a manufacturer to ensure they have rigorous quality control systems in place?

## Slide 17
Go / No Go?
The required thickness for the legs of a flat packed table is 25mm
Four legs are measured – the tolerance is +/- 0.5mm
Are they Go or No Go?
  Leg 1: 25.46mm
  Leg 2: 24.42mm
  Leg 3: 25.51mm
  Leg 4: 24.68mm

## Slide 18
Go / No Go?
The required thickness for the legs of a flat packed table is 25mm
Four legs are measured – the tolerance is +/- 0.5mm
Are they Go or No Go?
  Leg 1: 25.46mm Go
  Leg 2: 24.42mm No Go
  Leg 3: 25.51mm No Go
  Leg 4: 24.68mm Go
  What might be the consequences if the table leg doesn’t fall within tolerance?

## Slide 19
Marking out tools
Accurate measuring and marking out ensures quality products are made within tolerance
  Identify each of the tools below?

## Slide 20
Marking out tools
Explain how each tool is used for marking out
Try square
Sliding bevel
Steel rule
Mitre square
Marking gauge

## Slide 21
Reducing waste
Cutting parts or components from the edge of a piece of material saves space and reduces wastage
  Consider the following options to cut six wooden components

## Slide 22
Tessellation
Nesting shapes is a process that limits the amount of waste material by closely grouping them together
  Using nesting revises the same plan to include 20 components, increasing efficiency and reducing waste

## Slide 23
Datum points
A datum is a point from which all measurements are taken
  A datum symbol may be used to show the square face side and face edge of a piece of timber
  Graphic illustrations may use a datum to show which point a measurement was taken from

## Slide 24
Grain and pattern matching
A set of kitchen cabinet door fronts is marked out on a single sheet of natural wood
  Why was a more efficient cutting plan not chosen to reduce waste?
  Other than for aesthetic reasons, how might the direction of the grain be a consideration when marking out timber for making products?
  What other factors might influence how pieces are laid out on timber and potentially increase waste?

## Slide 25
Joint overlap
A joint is often created with each plank protruding slightly beyond the edge of the joint
  This makes allowances for planing and sanding to make the joint perfectly smooth
  If 1mm of material is wasted with each cut due to the kerf of the saw, how might this affect the way the joint is measured or cut?

## Slide 26
Surface treatments and finishes
Wood can be protected and visually enhanced using:
  Paint
  Wax
  Oil
  Stain
  Varnish
  Shellac
  Preservative
Finishes can be applied by brushing, rubbing or spraying
  Suggest finishes for a garden shed, a model wooden boat and a cricket bat

## Slide 27
Enhancing the appearance
As well as improving the function, finishes can make a product more appealing
  How would you enhance the natural grain of wood?
  Why would you choose to paint a child’s toy rather than leaving it bare?

## Slide 28
Wood preservation
Treating timber can help extend its life for decades
Wood preservative can be applied by hand or it can be bought pre-treated or ‘tantalised’
  Tanalised timber uses hydraulic pressure to force preservative into the timber which delays the rotting process and protects against insect and fungal attack
  Where might you find tantalised timber in use?

## Slide 29
Commercial finishing
Modern finishes can extend the life of timber based products
  Products can be sprayed by hand or machine
  Patterns, logos or wording can be printed onto the surface
  One of the fastest ways of painting is using a ‘curtain coater’ which gives a smooth and even coat
  What are the advantages of applying a finish on a production line?

## Slide 30
Environmental impacts
Traditional paints and finishes can have harmful effects on the environment
  Oil or solvent based products offer long lasting finishes, but contain high levels of VOCs – Volatile Organic Compounds
  Water based products are kinder to the environment
  What items of PPE would you use when using a solvent based finish on a wooden floor?

## Slide 31
Worksheet 4
Complete Task 2 on your Worksheet

## Slide 32
Plenary
How has machinery improved the production of mass produced timber components?
What are the key characteristics of:
  One off production
  Batch production
  Mass production
  Continuous production
Why are tolerances so important to check as part of the quality control process?